## Slide 1: Measurement 1: Estimating Emissions
Green software use on HPC

## Slide 2: Questions
How are emissions measured and classified under the GHG protocol?
How do I use the GHG protocol to estimate emissions from my use of HPC?

## Slide 3: Objectives
Understand how emissions are classified in the widely-used GHG protocol.
Know which GHG protocol classifications are relevant to use of HPC systems.
Learn a methodology to use GHG protocol to estimate the emissions associated with our use of HPC systems.
Understand how emission rates from HPC can be calculated.

## Slide 4: Greenhouse Gas (GHG) Protocol
The Greenhouse Gas protocol is the most widely used and internationally recognised greenhouse gas accounting standard
  Using the GHG protocol allows us to compare our emissions from use of HPC systems to other sources of emissions in a quantitative way
Scope 1: Direct emissions from operations owned or controlled by the reporting organisation, such as on-site fuel combustion or fleet vehicles.
Scope 2: Indirect emissions related to emission generation of purchased energy, such as heat and electricity.
Scope 3: Other indirect emissions from all the other activities you are engaged in. Scope 3 emissions are typically split into two further categories: upstream emissions and downstream emissions:
  Upstream scope 3 emissions: Includes all emissions from an organisation’s supply chain, e.g. emissions from manufacturing and shipping a product
  Downstream scope 3 emissions: Emissions resulting from the use of a product, e.g. the electricity customers may consume when using your product or waste output from the product

## Slide 5: Exercise: What scope for HPC emissions?
Throughout this lesson, we have spoken about emissions from two different sources associated with our use of HPC:
Emissions from the electricity used to run our models/simulations on HPC systems
Embodied emissions from the HPC system hardware.
Given the definitions of scope 1-3 emissions given above, which scope(s) do you think these two different sources of HPC system use emissions fall into?

## Slide 6: Solution
Emissions from the electricity used would be classified as scope 2 emissions.
Embodied emissions from HPC system hardware would be classified as upstream scope 3 emissions.

## Slide 7: How to estimate HPC emissions
Step by step process for estimating emissions:
Gather energy use
Determine local carbon intensity
Calculate embodied emissions
Compute HPC use emissions (HPC-E)
HPC-E = (E × CI) + M
E – Energy use
CI – Local carbon intensity
M – Embodied emissions

## Slide 8: 1. Gather energy use
You can get energy use by estimating it from total power draws or, sometimes, you can get it directly from the scheduler itself
We will look at two approaches for estimating energy use:
  Use the total power draw of the system
  Use the per-component power draw
If you can get this directly from measurements, this may be easier
  e.g. The Slurm scheduler may report energy use
  You may still need to estimate energy use from other components and overheads

## Slide 9: Estimate energy use: from total
One of the simplest ways to estimate your energy use is to use the total power draw of the HPC system and divide it by the number of components
  Gives a per component power draw that can be used to estimate energy use
Example: total power draw of 250 kW and 512 GPU cards
  Mean power draw per GPU = 250 / 512 = 0.488 kW/GPU
  Energy use of 2 GPU for 12 hours = 2 × 12 × 0.488 = 11.7 kWh
You should use the component your resource is allocated in to do the calculation
The total power draw can include other components (e.g. storage) and overheads from plant

## Slide 10: Estimate energy use: per component
Component | Count | Loaded power draw per unit (kW) | Loaded power draw (kW) | % Total | Notes
Compute nodes | 5,860 nodes | 0.41 | 2,400 | 85% | Measured by on system counters
Interconnect switches | 768 switches | 0.24 | 240 | 9% | Measured by on system counters
Lustre storage | 5 file systems | 8 | 40 | 1% | Estimate from vendor
NFS storage | 4 file systems | 8 | 32 | 1% | Estimate from vendor
Coolant distribution units | 6 CDU | 16 | 96 | 3% | Estimate from vendor
Total |  |  | 2,808 | 99% | 
Example for ARCHER2, data from measurement and estimates
We can use this data in the same way as we did to get mean per-node power draw, however:
On ARCHER2 we have compute node energy use per job
We know that compute nodes are around 85% of total power draw
We can add an extra 15% of energy use to the measured value to include electricity use from other components

## Slide 11: Estimate energy use: overheads
Plant overheads (cooling, transformation) also need to be included
PUE value gives this value: PUE 1.25 means 25% extra energy
PUE varies with time but not many site publish instantaneous values
  Usually end up using mean values
Example: ARCHER2 mean annual PUE is 1.1 so add 10% extra energy

## Slide 12: 2. Determine local carbon intensity
For the UK, you can use: Carbon Intensity API
  Reports carbon intensity every 30 minutes
In the first instance, fine to use an annual mean value
Some sites may use actual value (this is the approach on ARCHER2)
Type | Regions | Carbon Intensity (gCO2e/kWh)
Low | N. Scotland, S. Scotland, N.E. England, N.W. England | 22 - 48
Low Medium | N. Wales | 77
Medium | E. England, London, W. Midlands, S.E. England, Yorkshire | 108 - 135
High Medium | S. England, E. Midlands | 186 - 203
High | S.W. England, S. Wales, | 242 - 255
Mean values for 2024

## Slide 13: 3. Determine embodied emissions
Can be more difficult – data sources are less certain
If you are lucky, the HPC system may have done this for you!
If you need to do this yourself, the most important components are likely to be:
  Compute nodes
  Interconnect switches
  Storage
Rules of thumb
  The more complex the component, the higher the embodied emissions
  The more of something there is, the more important it is to consider

## Slide 14: Example: ARCHER2 embodied emissions
Component | Count | Estimated kgCO2e per unit | Estimated kgCO2e | % Total Scope 3 | References
Compute nodes | 5,860 nodes | 955 | 5,600,000 | 85% | (1)
Interconnect switches | 768 switches | 280 | 216,000 | 3% | (2)
Lustre HDD | 19,759,200 GB | 0.02 | 400,000 | 6% | (3)
Lustre SSD | 1,900,800 GB | 0.16 | 300,000 | 5% | (3)
NFS HDD | 3,240,000 GB | 0.02 | 70,000 | 1% | (3)
Total |  |  | 6,586,000 | 100% | 
Notes:
Large uncertainties in embodied emissions
Embodied emissions from data centre itself not included – thought to be less significant due to building/plant long lifespans
References
IRISCAST Final Report
Estimate taken from IBM z16(TM) multi frame 24-port Ethernet Switch Product Carbon Footprint
Tannu and Nair, 2023

## Slide 15: Example: ARCHER2 embodied emissions rate
We have the total embodied emissions for ARCHER2, how can we use this to get emissions per job?
Amortisation: divide total emissions by total resource available
ARCHER2 allocates in nodeh, total nodeh available:
6 years × 365 days × 24 hours × 5860 nodes = 308,001,600 nodeh
Embodied emissions kgCO2e/nodeh:
6,586,000 kgCO2e / 308,001,600 nodeh = 0.021 kgCO2e/nodeh

## Slide 16: 4. Compute total emissions
ARCHER2 job example:
E:
  Measure compute node energy use
  Add 15% for other components
  Add 10% for plant overheads
CI:
  Take CI at start of each job and use this
M:
  Use nodeh from the job and embodied emissions rate to compute M
Plug all the numbers in and compute the per-job emissions
Sum over all jobs in the set to get total emissions
HPC-E = (E × CI) + M
E – Energy use
CI – Local carbon intensity
M – Embodied emissions

## Slide 17: Exercise: compute HPC emissions
You are using (or running) a GPU-based HPC service and a particular project has used the following amounts of resource:
  1,100 GPUh
  3,542,000 kWh
The total embodied emissions for the service are 6,500,000 kgCO2e, the service lifetime is 7 years and there are 1000 compute nodes each with 8 GPUs. The service is hosted in a location with a carbon intensity of 40 gCO2e/kWh.
Compute the scope 2 emissions for the project use
Compute the scope 3 emissions rate in kgCO2e/GPUh
Compute the scope 3 emissions for the project use
Compute the total emissions for the project use
Do scope 2 or scope 3 emissions dominate or are they evenly matched?

## Slide 18: Solution
Operational emissions (Scope 2): E×CI = 3,542,000 kWh × 0.040 kgCO2e/kWh = 141,680 kgCO2e
Total resource: 7 years × 365 days × 24 hours × 1000 nodes × 8 GPU per node = 490,560,000 GPUh Embodied emissions rate: 6,500,000 kgCO2e / 490,560,000 GPUh = 0.01325 kgCO2e/GPUh
Embodied emissions (Scope 3): M = 1,100 GPUh × 0.013 kgCO2e/GPUh = 14.575 kgCO2e
Total emissions: HPC-E = 141,680 + 14.575 = 141,696 kgCO2e
Scope 2 emissions dominate