## Slide 1: Measurement 2: HPC-CI
Green software use on HPC

## Slide 2: Introduction
The HPC Carbon Intensity (HPC-CI) metric is a methodology to estimate your emissions rate from HPC use
It also allows you to measure progress to reducing or eliminating emissions
HPC-CI does not replace the GHG – it is a more specific metric aimed at computing a rate of emissions from HPC system use
The HPC-CI definition is heavily influenced by the Green Software Foundation Software Carbon Intensity (SCI) metric

## Slide 3: The HPC-CI equation
The HPC-CI equation is very closely related to the way in which we calculated emissions from HPC systems earlier
HPC-CI = [(E × CI) + M] per R
E – Energy use
CI – Local carbon intensity
M – Embodied emissions
The new term is R – the functional unit
  This is a definition of the output from the work that generated the emissions
  Examples: iterations, simulated time, calculation cycles, research papers published, resources used, cost

## Slide 4: Calculating HPC-CI
The steps to calculate the HPC-CI start with the process we already discussed for computing emissions
Compute HPC-E
  Gather energy use
  Determine local carbon intensity
  Calculate embodied emissions
  Compute HPC use emissions (HPC-E)
Select your functional unit
Calculate your HPC-CI rate

## Slide 5: Select your functional unit
The metric does not specify what you should use as a functional unit
You can choose functional units that best represents output from your use of HPC systems
  You can even have multiple HPC-CI rates with different functional units for different uses
Examples
  A metric from the software you use: ns simulated, years simulated, iterations
  A metric tied to research progress: number of compounds modelled, data points analysed, papers published

## Slide 6: Exercise: Calculating HPC-CI
In the previous exercise we computed the total HPC system emissions for 3 months of project use to be 141,695 kgCO2e. The project was modelling the climate and managed to simulate 3,680 years of Earth’s climate during that 3 month period using 1,100 GPUh of resource.
What is the HPC-CI in kgCO2e per simulated year?
What is the HPC-CI in kgCO2e per GPUh?

## Slide 7: Solution
Given by: 141,695 kgCO2e / 3,680 simulated years = 38.5 kgCO2e/simulated year
Given by: 141,695 kgCO2e / 1,100 GPUh = 128.8 kgCO2e/GPUh

## Slide 8: Improving the HPC-CI rate
You cannot improve the HPC-CI rate by purchasing offsets
  Offsets do have an important role in a Net Zero strategy but are not carbon eliminations
If you make your HPC use more energy efficient, hardware efficient, or carbon aware, your HPC-CI rate will improve
  Investing time or resources into one of these three principles is the only way to reduce the HPC-CI rate.

## Slide 9: Estimating future emissions
Our HPC-CI rate can also be used to predict emissions from future or proposed work
This can be useful in choosing a strategy for proposed work to minimise emissions and to respond to funder questions around quantifying emissions.

## Slide 10: Key points
The GHG protocol is a metric for measuring an organisation’s total carbon emissions and is used by organisations all over the world.
The GHG protocol puts carbon emissions into three scopes. Scope 3, also known as value chain emissions, refers to the emissions from organisations that supply others in a chain. In this way, one organisation’s scope 1 and 2 will sum up into another organization’s scope 3.
You can use the GHG protocol to estimate your emissions from HPC system use but it requires access to reasonable quality information from the HPC systems you are using.
The HPC-CI is a metric designed specifically to calculate emissions from HPC systems and is a rate rather than a total. This can be used to measure improvements in emissions efficiency and drive reductions in emissions.